## Slide 1: Title
A novel approach for efficient resource allocation in 6G V2V networks
using neighbor-aware greedy algorithm and sweep line model
Authors: Spandana Mande, Nandhakumar Ramachandran
Journal: Egyptian Informatics Journal, 2025

## Slide 2: Background
V2V / V2X networks are critical for autonomous driving & ITS.
Challenges in 6G V2V: High mobility, Dense traffic, Low latency needs.
Existing solutions (RSU-based, centralized allocation) cause delay, interference, and collisions.

## Slide 3: Problem Statement
How to allocate resources efficiently in 6G V2V?
Goals: Reduce latency, Improve throughput & QoS, Ensure secure communication.

## Slide 4: Proposed Solution
NNAGbRD-V2V-SLM (Neighbor Node Associated Greedy + Sweep Line Model):
1. Neighbor nodes help allocate resources.
2. Greedy algorithm selects best resource quickly.
3. Sweep line model optimizes allocation paths.

## Slide 5: Three Scenarios
1. Full Resources (V2V-RD-FSR): Allocate when enough for all.
2. Partial Resources (V2V-RD-PSR): Fair distribution when limited.
3. Time-Sharing (V2V-RD-TS): Vehicles share resources by time slots.

## Slide 6: Key Formula 1: Vehicle Registration
VData[Vn] = (Σ Vlocv) / (π·δ(Vn)) + τ
Registers vehicles in the network. δ(Vn)=vehicle count, τ=threshold.

## Slide 7: Key Formula 2: Resource Capacity
Rmax[Rn] = maxR (Σ Ridr / Rmaxalloc)·β + Th
Maximum vehicles a resource can support. β=allocation range, Th=threshold.

## Slide 8: Key Formula 3: Registration with Distance
μ(VData(N)) = (Σ(Vlocr+λr)) / (D(γ)² + N·log(1+δ(Vn)/max(τ)))
Registers vehicles/resources with distance + subband range.

## Slide 9: Key Formula 4: Neighbor Node Selection
NeiVN(Vr|Vlocr) = [Σγv + ΣVv2v·ω(Vr+Vr+1)]/(Σ(minγ-maxγ)) + (μ/2)·max(R)
Selects nearest neighbor vehicle for distributed allocation.

## Slide 10: Key Formula 5: V2V Linking
Link(ω) = Σ Σ max(Vr·Rv + L(v,min(D(v+1))))
Establishes V2V communication links for sharing resources.

## Slide 11: Key Formula 6: Resource Allocation
Ralloc[Vn] = Π (Σ Rset + min(D(v,v+1))) / H(Cset)
Assigns resource blocks dynamically. H(Cset)=channel set.

## Slide 12: Key Formula 7: Delay Handling
ΔRset = δ(R)/2 [max(VTi)] + [Vlinki+1 - max(Vlink)M,Nei]
Reduces latency during allocation.

## Slide 13: Key Formula 8: Time Sharing
Ralloc[Vn] = Π (Σ(Rset + Vr·T(v))) / H(Cset)
Allocates resources based on time slots when demand > supply.

## Slide 14: Sweep Line Model
Imaginary vertical line swept across vehicles.
Detects intersections, nearest neighbors, conflicts.
Reduces complexity to O(n log n).
Optimizes resource distribution path.

## Slide 15: Simulation Setup
Simulator: NS3 + SUMO
Area: 200x200 m, Nodes: 20 vehicles
Traffic: TCP, Protocol: AODV
Metrics: Latency, Throughput, Packet Delivery Ratio

## Slide 16: Results
Neighbor node selection accuracy ↑
Vehicle link establishment delay ↓
Resource distribution accuracy ↑
Sweep line reduces allocation time (O(n log n))
Better than Greedy Cellular V2V Link Selection Algorithm.

## Slide 17: Conclusion
NNAGbRD-V2V-SLM improves latency & resource allocation.
Efficient neighbor node use, not only RSUs.
Handles full, partial, and time-shared resources.
Future: Extend to ultra-dense mobility scenarios.